## Slide 1: Campus Convening on Climate Change
STRATEGIC PLAN: MSU 2030
RESEARCH IN ENERGY AND MATERIALS
May 25, 2022

## Slide 2: Agenda:
STRATEGIC PLAN: MSU 2030
Opening remarks – Doug Gage, VP for Research and Innovation
Introductions – Doug Buhler, AVP Research and Innovation
Research flash talks:
Qingxu “Bill” Jin, assistant professor in the Department of Civil and Environmental Engineering
Annick Anctil, associate professor in the Department of Civil and Environmental Engineering
Dong Zhao, associate professor, Construction Management - School of Planning Design and Construction
Eric Hegg, professor, Department of Biochemistry and Molecular Biology, and Associate Dean for Research College of Natural Science
Justin Kirkpatrick, assistant professor in the Department of Economics
Networking – table conversations

## Slide 3: Flash talks
STRATEGIC PLAN: MSU 2030
First up – Bill Jin

## Slide 4: What do we as civil engineers do?
What our friends think we do.
What our parents think we do.
What the society thinks we do.
What our bosses thinks we do.
What we imagine we do.
What do we actually do?
PI: Qingxu “Bill” Jin
billjin@egr.msu.edu
PhD: Xiaoqiang “Antonio” Ni
MS: Quentin Greiner
EnSURE: Luke Naughton
Resilient, Intelligent, Sustainable & Energy-efficient (RISE) Infrastructure Materials Lab
Civil and Environmental Engineering
Materials with low carbon footprint
“Smart” Bendable Concrete
Infrastructure Sustainability
Infrastructure Resiliency
Climate Mitigation
Climate Adaptation

## Slide 5: Built environment has high carbon footprint
Construction Materials
We need to mitigate climate change

## Slide 6: Mitigate climate change through low carbon materials
Alternative cementitious material
Xu K., Jin, Q., et al.
Recycled industrial and construction waste
Paul A., Jin, Q., et al.
Biofuel residues
Li J., Jin, Q., et al. 2022
Jin, Q. and Ma H.
Coal ashes

## Slide 7: Climate disasters demand resilient built environment
We need to adapt to climate change

## Slide 8: Adapt to climate change through resilient and smart materials
d) Self-sensing
(a) Ultra-ductility
(b) Cracking
resistance
(c) Self-healing
Jin, Q. and Li VC. 2019; Jin, Q. and Li VC. 2020; Li and Li 2019; Li 2019
Resilient Infrastructure that adapt to extreme events
Kesner and Billington 2002
Climate-driven natural disasters

## Slide 9: Combat climate change through collaborations
Materials
Science & Design
Resilient Infrastructure
Climate-driven disasters
Data collection
Machine learning
LCA
3D printing construction
Disaster characterization
Climate model
Policy

## Slide 10: Next Up Annick Antcil
STRATEGIC PLAN: MSU 2030
Next up – Annick Anctil

## Slide 11: Annick Anctil: Sustainable Energy Systems
Material Processing
End-of-life
Mining
Manufacturing / Assembly
Use Phase
Coal
Natural gas
Nuclear
Renewable
Prospective LCA: evaluate new technology to reduce unintended consequences

## Slide 12: Environmental impact of PV manufacturing
What is the environmental impact of producing silicon solar PV modules in US?
Impact of sand extraction
Impact of grid decarbonization on manufacturing
Impact of module manufacturing
Heidari, S. M., & Anctil, A. (2022). Resources, Conservation and Recycling, 180, 106171.
Notes: Compare the impact of us vs china manufacturing based on material mining transport and local electricity grid

## Slide 13: Transparent Organic Photovoltaics
Net energy and cost-benefit of transparent PV in building-integrated applications
Anctil, A., Lee, E., & Lunt, R. R. (2020). Applied Energy, 261, 114429.
Reducing impact material manufacturing
E Lee, CJ Andrews, A Anctil, ACS Sustainable Chemistry & Engineering 6 (7), 8230-8237 (2018)
LCA + toxicity + green chemistry
Iterative approach to reduce environmental, cost and chemical hazard
Notes: LCA considers both the energy change in the building and the electricity production from the PV to calculate the net energy benefit

## Slide 14: LCA of 2nd life battery from EV
Battery testing
Kamath, D., et al. (2020). Environmental Science & Technology, 54(11), 6878-6887
Kamath, D., et al.. (2020). Waste Management, 113, 497-507.
Cost and carbon footprint of second-life battery in residential and utility-level applications
Interactive decision tool for battery storage (1st and 2nd life battery) + solar system design for various applications
In progress: Interactive decision tool for battery recycling
Notes: Evaluate the technical, economic and environmental feasibility of using end of life battery for stationary applications in various locations

## Slide 15: Projects & Interests
How can we reduce the environmental impact of new (energy) technologies?
Collaborations

## Slide 16: Next up Dong Zhao
STRATEGIC PLAN: MSU 2030
Next up – Dong Zhao

## Slide 17: Dong Zhao
Associate Professor of Construction Management and Civil Engineering
School of Planning, Design & Construction
Human-building integration
Green and smart buildings
Building digital modeling
dzhao@msu.edu
www.msu.edu/~dzhao

## Slide 18: Routine Occupant Behavior Capture

## Slide 19: Large Scale Building Energy Retrofit

## Slide 20: EV and Charging Infrastructure
Notes: EV-related construction.
EVs have almost zero emissions, which greatly improves environmental sustainability for the U.S. where 29% of greenhouse gas emissions are from vehicles. 18.7 million EVs are estimated to be on U.S. roads by 2030 with a 37% annual growth, based on the McKinsey Center for Future Mobility. China has the largest number of EVs in the world and maintains a 35% annual increase in EV sales [5]. Moreover, major auto manufacturers including General Motors, Ford, and Chrysler are committed to an all-EV future in the next 20 years.
The construction cost of distribution lines are too high. No new grid construction is suggested.
When choosing a small battery size, every charging station needs a batter storage unit.
A combination of a small number of but big size of battery units is preferred to reduce costs
EV-integrated buildings (homes, commercials) - Architecture
Regional sustainable and equitable development - We can work with urban planning and public policy.
Atlanta EV Toyota, Mercedes

## Slide 21: Future Research
Design and Construction of EV integrated buildings and infrastructure
IoT-based commercial building retrofit
Digital Twin and human factors in the sustainable built environment
Notes: EV-related construction.
EVs have almost zero emissions, which greatly improves environmental sustainability for the U.S. where 29% of greenhouse gas emissions are from vehicles. 18.7 million EVs are estimated to be on U.S. roads by 2030 with a 37% annual growth, based on the McKinsey Center for Future Mobility. China has the largest number of EVs in the world and maintains a 35% annual increase in EV sales [5]. Moreover, major auto manufacturers including General Motors, Ford, and Chrysler are committed to an all-EV future in the next 20 years.
The construction cost of distribution lines are too high. No new grid construction is suggested.
When choosing a small battery size, every charging station needs a batter storage unit.
A combination of a small number of but big size of battery units is preferred to reduce costs
EV-integrated buildings (homes, commercials) - Architecture
Regional sustainable and equitable development - We can work with urban planning and public policy.
Atlanta EV Toyota, Mercedes

## Slide 22: Next up Eric Hegg
STRATEGIC PLAN: MSU 2030
Next up – Eric Hegg

## Slide 23: Ammonia as a fuel
Ammonia as a Fuel
Capture
Sunlight is most abundant energy resource, but diffuse and intermittent
Convert
Solar electricity can be concentrated and stored in chemical bonds by splitting water (the most abundant molecule on Earths surface)
Store / Distribute
Hydrogen is hard to store and distribute. It can be combined with nitrogen (the most abundant molecule in the atmosphere) to make ammonia which is already stored and disturbed globally at large scale
Use (our vision)
We are investigating conversion of ammonia back to H2 or electricity to complete the renewable energy cycle.
2 H+(aq) + 2 e– → H2(g) H2O(l) → ½ O2(g) + 2 H+(aq) + 2 e–
N2 + 3 H2  2 NH3
Haber Bosch is >80% efficient

## Slide 24: Ammonia Storage and Electrolysis
Focusing on the most energy intensive step in N2  NH3 conversion: addition of the first two H-atoms
Pairwise addition of H-atoms to N2 via H-bonding lowers thermodynamic barriers for N2 reduction.
Warren and co-workers
J. Am. Chem. Soc. 2021, 143, 15960.
New molecular catalysts based on earth abundant metals release energy from NH3 via electrocatalysts:
Simple and robust catalysts that function in liquid ammonia
Warren and co-workers: ChemRxiv 2019; under review
Ammonia Storage and Electrolysis
Warren Lab (Chemistry)

## Slide 25: Ammonia Storage and Electrolysis continued
Ammonia Storage and Electrolysis
Hamann and Smith (Chemistry) discovered way to store liquid ammonia at room temperature and ambient pressure which can be electrolyzed to produce hydrogen on demand
Hamann and Smith Groups (Chemistry) reported first molecular electrocatalyst for ammonia oxidation
Proceedings of the National Academy of Science 2019, 116 (8) 2849–2853
Joule 2022, 6, 1 – 10

## Slide 26: Biological Nitrogen Dioxide Reduction to Ammonium
Biological NO2- Reduction to NH4+
NO2- + 8H+ + 6e- → NH4+ + 2H2O

## Slide 27: Biological Nitrogen Dioxide Reduction to Ammonium Continued
Biological NO2- Reduction to NH4+
NO2- + 8H+ + 6e- → NH4+ + 2H2O
Perform the reaction inside of biological organelle to trap and concentrate NH4+
Hegg Lab (Biochemistry)

## Slide 28: Next up Justin Kirkpatrick
STRATEGIC PLAN: MSU 2030
Next up – Justin Kirkpatrick

## Slide 29: Justin Kirkpatrick
College of Social Science
Department of Economics
Energy + Environmental Economics

## Slide 30: Research
How households make decisions about energy consumption and investment
How these household decisions, in aggregate, affect the grid
  Price of electricity
  Pollution + carbon emissions
  Distributional concerns
Source: TheStreet.com

## Slide 31: Why are these interesting? Why economics?
Households make trade-offs between $ and electricity.
  Knowing how households do this is useful
    Predict behavior
    Value things without prices
But these are made “through a fun-house mirror”
  Rates households pay are disconnected from actual cost
    Real-time vs. constant
    Fixed cost recovery
    Pollution + carbon emissions
  Wholesale market (beyond households)
    Market power
    Long-run plant construction

## Slide 32: Some prior research
Price effect of battery storage
  Wholesale electricity markets
  I estimate around 2.2% decline in wholesale power prices during evening hours
  But zero effect for “Tesla Powerwalls” owned by private households
Solar siting
  Where a panel is installed determines
    How much solar is generated
    What generator is actually offset
  “Dollarize” total value of panel

## Slide 33: Call for collaboration
Anywhere a project
Needs to consider consumer behavior
Needs to value something beyond the “market price”
Market power + battery characteristics
  Power and energy both affect how a battery alters the market
Perceptions of household storage
  Operate to max. cost savings?
  Operate to min. grid consumption? (TOU pricing)
  Substitute for backup generator

## Slide 34: Questions?
STRATEGIC PLAN: MSU 2030
Time to network!